## Slide 1
The ESA Scout framework
1st EO Commercialisation Forum
Jean-Pascal Lejault (Scout project manager)
SCO-HO-ESA-PM-0054
30th October 2023

## Slide 2: Scout framework
New category of research missions in Earth Observation since 2019, inspired by New Space
  to prove new disruptive concepts and to timely deliver innovative science
  Scout missions are science-driven, not commercially-driven
    However, Scout missions may have commercial applications
      It can’t just be the dominant factor in the mission selection
Main features
  a more pro-active role of industry (service contract with limited oversight from ESA)
  a low-cost approach: 30 M€ e.c. 2022 max (use of COTS, lighter model philosophy, strictly tailored ECSS standards, lean reviews)
  a rapid development cycle (3 years from start of phase B/C/D/E1 implementation to launch).

## Slide 3: Main Scout features
Fully funded End-to-end service contract
  The Contractor shall procure, develop, validate, launch, operate and complete the entire system (ground segment, space segment, launch services and operations)
    The satellite(s) remain(s) the property of the Contractor
  Key Performance Gate Reviews (KPGR) at key stages (e.g. SRR, PDR, CDR, QR)  to raise confidence that the service will be delivered as expected
    In case a KPGR fails, ESA has the right to terminate the Contract
Which service?
  delivery of innovative science products
  specified in the Mission Requirements Document (MRD)
  free and open data policy

## Slide 4: Process followed for the first Scout cycle
ITT to
  collect Scout mission concepts (some 16 concepts were received)
  down-select the most promising concepts (4 concepts)  system consolidation studies
Independent scientific assessment of the 4 down-selected concepts
Submission to the Programme Board for Earth Observation (PB-EO) for implementation
For each approved Scout mission
  Procurement (dialogue phase, RfQ, proposal writing, evaluation, negotiations)
  Implementation
Typical time scales
  1.5 years between ITT and ACEO conclusions
  1 year between PB-EO approval and phase B/C/D/E1 kick-off

## Slide 5: CubeMAP (Scout-1)
A constellation of 3 12U satellites to observe key radiative gases in the atmosphere
  H2O, CO2, CH4, O3, N2O
Sadly, CubeMAP could no longer be maintained within the Scout framework  contract terminated in Q2 2023
  Full Lessons learnt are being collected

## Slide 6: HydroGNSS (Scout-2)
Aim: improve our knowledge of the Earth water cycle.
Technique: GNSS reflectometry (i.e. sense the signals reflected by the Earth surface from GNSS satellites)
Constellation of two small satellites (50 x 50 x 70 cm, 70 kg)
Sun synchronous orbit, 550 km altitude
Launch readiness: Q4 2024
Service (science data) for up to 4.5 years
  soil moisture
  inundation / wetlands
  soil freeze / thaw (notably over permafrost)
  above-ground biomass
Potential interest in adding satellites to deliver a commercial service to specific customers (e.g. soil moisture knowledge and prediction for agriculture to adapt irrigation and manage water shortage or over-abundance)

## Slide 7: Opportunities for commercialisation
Scaling-up
  It is easy to add recurring satellites to a Scout mission at a low-cost (not to be paid by ESA)
    to replace satellites nearing end-of-life
    to improve the science return once the concept is demonstrated
      (e.g. improve coverage or reduce revisit time)
    to expand the science products to commercial applications (e.g. Green transition and sustainability regulations)
Commercial applications, though not at the heart of the selection of Scout missions, are relevant
  To address commercial needs which can be built on the science service
  An incremental approach (Minimum Viable Product) is very suitable:
    Start with “basic” commercial service directly derived from the science products
    Add one recurring satellite to expand the commercial service
    Then add more recurring satellites as the commercial service further grows
   Financial risks can be minimized

## Slide 8: Conclusion
The Scout framework offers key opportunities for Industry in Europe, including commercialisation
Commercial applications
  can be incrementally derived from the science products at a low cost
  minimise risks as initial development is fully funded and supported by ESA experts
  maximise return on investment
Next step for Scout is coming very soon and will be discussed at the PB-EO meeting on 21-22 November 2023
  Stay tuned!
Visit https://www.esa.int/Applications/Observing_the_Earth/FutureEO/Scouts_ESA_s_agile_research_missions

## Slide 9
Thank you for your attention

## Slide 10
Backup slides

## Slide 11: Commercial possibilities with HydroGNSS
Agriculture: soil moisture knowledge and prediction is vital for agriculture, especially under changing climate conditions and demographic pressures.
  Quantification of water shortage or over-abundance allows for correct irrigation and drainage.
  This is important locally (farm planning) and at a larger scale (regionally and nationally).
Water agencies extract from aquifers and natural reservoirs, which have a dependence on rainfall and soil moisture.
  Run-off from land into lakes and water courses can cause water treatment facilities to overflow, causing river pollution.
  Construction site flooding can cause pollutant discharge (silt, oil, chemicals), as well as halting progress.
Flood planning agencies need to know the saturation levels of soils to predict risks of flooding, something also important to insurance companies
Weather forecast: accurate numerical weather predictions (NWP) depends on soil moisture knowledge
  Soil moisture has a significant effect on weather, especially over large land masses.
Insurance industry
  interest in the risk of land subsidence caused by cycles in soil moisture, especially in hilly and mountainous regions.
Management of infrastructure
  Changes in freeze/thaw cycle and underlying permafrost cause subsidence for some settlements in high latitudes.
Notes: Silt  limon (en français)

## Slide 12: Scout future
360-degree Scout lessons learnt exercise on-going, report due by 3rd Nov 2023
  To improve the next Scout cycle based on the experience from the first cycle
    e.g. reduce time-to-contract duration, streamline procurement process
  To improve the Scout framework to maintain attractiveness (ESA Member States & Industry)
November 2023 PB-EO
  Present the outcome of the Scout lessons learnt exercise
  Agree with Member States the approach for the next Scout cycle and next steps

## Slide 13: Scout specificities
New Space approach
MRD: key document, defining the service to be delivered
  produced by the Prime Contractor and delivered as part of the proposal
  MRD is co-signed by all parties (ESA, Contractor, SAG chair) at phase B/C/D/E1 kick-off
Other requirements are strictly limited to best fit the Prime Contractor’s processes
  ECSS standards are significantly tailored to fit to New Space
  No dedicated management requirements, only limited management tasks in the SoW
  Product Assurance requirements are tailored
Lean ESA reviews
  ESA project-level reviews, no ESA independent teams
Lean ESA team, as ESA relies much more on Industry for Scout missions
  Very pragmatic and flexible Scout project team
  Dedicated expert support in the areas exposed to the main risks